# PRODUCT SPECIFICATIONS

Sealing of joints in structures with window foil.

Item	.....	Preliminary treatment of the subsurface

Clean the joint surface mechanically. The subsurface needs to be dry, free of dust, loose bits, oils, greases or other contamination which could act as release agent.

............rm.	Price ............ €	Total Price ............ €

Item	.....	Sealing

Delivery and installation of an elastic window foil for the interior and aluminium coated, e.g. pinta fenband i alu.
Self-adhesive on one or both sides and tested according to the quality standards DIN EN 41083.
The window foil is compatible with all common building materials.

The foil possesses the following qualities:

- Free of plasticizers(softening agents), heavy metal, chlorine, bitumen, fibers, CFC, formaldehyde, PCB and emissions

- Fire class B2 according to DIN 4102

- Water vapor tight

The window foil is delivered on rolls.

Foil dimensions:  	          mm	width:     mm

Example: manufacturer

pinta abdichtung GmbH

The manufacturer´s instructions are to be observed.

............rm.	Price ............ €	Total Price ............ €